Authenticating packets in a provider independent network with IPSec-AH
Othmar Gsenger <otti-ff@graz.funkfeuer.at>
Christian Pointner <equinox@chaos-at-home.org>
Friedrich Lobenstock <fl@fl.priv.at>

---
Content
Introduction
Our Network
IPsec and Anycast
Implementation – Firmware
OLSR+BGP Outlook
The Big Picture

---
Introduction
Free network as independent as possible
Hand out public IP addresses for Internet access
Support different upstream providers
Protect against IP address high-jacking

---
Othmar Gsenger <otti-ff@graz.funkfeuer.at>
IPsec and Anycast

---
Our Network
One continuous wireless cloud
multi-home to different upstream providers
provider independent (PI) address space of public IP addresses

---
Routing
BGP border routers announce the hole public IP address range
At each border router there is an OLSR router, which announces the default route
No NAT or MASQUERADE

---
What's IPSec? - ESP
Security extension
for Ipv4 and IPv6
Adds an additional
header after the
IP header
Encapsulating Security Payload (ESP) encapsulates the encrypted payload and adds an authentication tag

---
IPSec AH
Authentication Header (AH)
adds a cryptographic checksum of the green parts, but doesn't encrypt the payload

---
IPSec tunnel mode?
Transport mode
Ipsec with IPIP tunnel
(Tunnel mode)
Ipsec with GRE
IPSec in tunnel mode is just using Ipsec with an IPIP tunnel

---
olsr default route
router checks AH
router checks AH

---
Why this isn't working
We want IPsec to add AH only when we use the default route
So we need a Security Association with all hosts, but the hosts in our routing table

---
Why this isn't working
What we want to do:
We
Host 1 on the internet
router checks and
removes AH
only we and the boarder
gateway know the secret
host 2 on the internet

---
Why this isn't working
What it looks like for IPsec
We
Host 1 on the internet
both need to know the session key to check the ah header
host 2 on the internet

---
Tunnel mode
shortest route to 10.10.0.5
HNA 10.10.0.5
router checks AH
and removes IP header
HNA 10.10.0.5
router checks AH
and removes IP header

---
Ping ...
IP 193.33.151.42 > 10.10.0.5: AH(spi=0x00000150,seq=0xc69): IP 193.33.151.42 > 129.27.3.16: ICMP echo request, id 36463, seq 0, length 64 (ipip-proto-4)
IP 10.10.0.5 > 193.33.151.42: AH(spi=0x00000150,seq=0x4a): IP 129.27.3.16 > 193.33.151.42: ICMP echo reply, id 36463, seq 0, length 64 (ipip-proto-4)
IP 193.33.151.42 > 10.10.0.5: AH(spi=0x00000150,seq=0xc6a): IP 193.33.151.42 > 129.27.3.16: ICMP echo request, id 36463, seq 256, length 64 (ipip-proto-4)
IP 10.10.0.5 > 193.33.151.42: AH(spi=0x00000150,seq=0x4b): IP 129.27.3.16 > 193.33.151.42: ICMP echo reply, id 36463, seq 256, length 64 (ipip-proto-4)

---
Difference to signed routing
Signed Routing
Authenticated Internet-Traffic
Protects internal routing tables
Asymmetric Cryptography
PKI
Protects data sent to the internet
Symmetric Cryptography
Upstream Provider creates keys

---
Possible attacks
Signed Routing
Authenticated Internet-Traffic
Inject data when you are on the route path
Manipulate routing table
Combine both if you can!

---
Provider neutrality
It's possible that multiple upstream-provider route their IP addresses into the network and protect them
Every provider may run one or multiple border routers (with anycast IPs)
Internal IP addressing stays valid and may be done by someone else.

---
Anycast
The border gateways have the same IP address and announce it with OLSR HNA
shorter route wins

---
Limits of Ipsec with anycast
IPSec wasn't designed to allow anycast host.
Replay protection is done by sequence numbers, but the anycast routers don't know each others sequence counter
so replay protection doesn't work

---
Limits of Ipsec with anycast
IPsec doesn't define a key management, but there is no anycast key management in existence
synchronization of keys can help, but only for hot standby systems (not for load balancing)
so we have to use static keying

---
Links to further infomation
building hot standby IPsec tunnels with key management
  - isakmpd
  - sasyncd
  - carp
building real anycast tunnels
  - http://www.anytun.org

---
Christian Pointner <equinox@chaos-at-home.org>
Implementation - Firmware

---
a story about penguins, swans and turtles
ipsec on linux2.4
and linux2.6

---
openswan - ipsec on linux2.4 (openwrt white russian)
consists of kernel module ond userspace ipsec tool
ipsec interface device
configuration through /etc/ipsec.conf

---
Problem
ipsec device is bound to existing interface
bypasses kernel routing table

---
Solution
bind ipsec device to a dummy ipip tunnel
trick ipsec to use routing table, therefore ip tunnel gets bypassed

---
configuration
# ip tunnel add dummy0 mode ipip local 127.0.0.1 remote 127.0.0.1
# ifconfig dummy0 193.33.151.42 up
/etc/ipsec.conf
config setup
        interfaces="ipsec0=dummy0"
        pluto=no
conn ff
        type=tunnel
        left=193.33.151.42
        right=10.10.0.5
        rightsubnet=0.0.0.0/0
        auto=manual
        auth=ah
        ah=hmac-sha1-96
        ahkey=0x0000000000000000000000000000000000000023
        spi=0x150
        authby=never
        ahreplay_window=0

---
kame-tools – ipsec on linux2.6
consists of userspace tool setkey and ike-daemon racoon
manipulate the kernel SAD and SPD through pf_key

---
configuration
/etc/ipsec-tools.conf (debian)
add 10.12.0.170 10.12.1.155 esp 0x123 -r 0
  -E aes-cbc 0x00000000000000000000000000000001
  -A hmac-sha1 0x0000000000000000000000000000000000000003;
add 10.12.1.155 10.12.0.170 esp 0x123 -r 0
  -E aes-cbc 0x00000000000000000000000000000002
  -A hmac-sha1 0x0000000000000000000000000000000000000004;
# Security policies
spdadd 10.12.1.155 10.12.0.170 4 -P in ipsec
        esp/transport//require;
spdadd 10.12.0.170 10.12.1.155 4 -P out ipsec
        esp/transport//require;

---
IPSec on Freifunk Firmware
kernel2.4 -> openswan
dummy ipip device
own package consisting of some scripts

---
Friedrich Lobenstock <fl@fl.priv.at>
OLSR+BGP4 Outlook

---
OLSR+BGP4 Outlook
Why BGP4 (Border Gateway Protocol 4)?
Why OLSR (Optimized Link State Routing)?
Why get BGP and OLSR talking?
OLSR to BGP protocol translation
Problems
The Future

---
Why BGP4 (Border Gateway Protocol 4)
The standard routing protocol on the Internet
BGP4 is essential when multi-homing with a PI(provider independent) address space to more than one upstream provider
We are now basically an ISP providing public IP addresses to our participants

---
Why OLSR (Optimized Link State Routing)?
A routing protocol optimized for ad-hoc wireless LANs - the currently defacto standard
Currently used because of support in Freifunk firmware for commodity wireless routers
In the future OSLR might be replaced by other protocols like BATMAN

---
Why get BGP and OLSR talking?
Border Gateways do not necessarily talk OSLR (i.e. Cisco Routers), but speak BGP
OLSR announces the gateways anycast IP but doesn't know anything about the conditions of upstreams - this info is in BGP
Status of eBGP session needs to influence announcement of anycast IP in OLSR

---
OLSR to BGP protocol translation
Each Border Gateway needs a companion router running OLSR which is only stable on MIPS platform
Current plan was to get OLSRD talking to the popular QUAGGA routing daemon
olsrd_quagga plug-in available for OLSRD which looked like a promising starting point

---
Problems and Pitfalls
olsrd_quagga plug-in communication with Quagga had to be fixed in our local Freifunk firmware version
Nonetheless OLSRD just crashes with this plug-in loaded and debugging led nowhere
Currently no conditional routing announcements implemented in OLSRD

---
The Future
Get olsr_quagga plug-in working
Implement conditional HNA announcements in OLSRD based on routing info from BGP(QUAGGA)
Motivate other projects like BATMAN to support such a communication with QUAGGA

---
The Big Picture
Multi-homed with public IP addresses
Network provider independet
IP addresses are protected
Network stays independent

---
Questions?